## Slide 1: Linux SMP versus AMP Data copy from core1 to core0.
Rod Frazer
August 2013

## Slide 2: Overview
In this example we contrive a trivial data exchange application where a producer thread creates data into a shared buffer that it passes over to a consumer thread. The shared buffer is configured in a ping pong arrangement so that while the producer thread is filling the next buffer, the consumer thread can drain the previous buffer. The buffer exchange is sequenced thru the use of exclusive locks to ensure that the buffers are exchanged in order and neither thread is allowed to pass the other in the exchange sequence.
This example is run on an SMP linux platform where a pure SMP implementation is run as you would expect. Then the example is run on the same SMP linux platform but simulating the effects of an AMP environment.

## Slide 3: SMP Overview
In the SMP example the application is run on the A9 dual core in SMP mode with core isolation such that the producer thread can be run with affinity on core 1 and the consumer thread is run with affinity on core 0. pthread_mutex_locks are used to ensure the sequencing between the two ping pong buffers. The producer thread writes incrementing values into the shared buffers to pass over to the consumer thread. The consumer thread is then configured to operate in three different ways:
No Work – do nothing, simply release the buffer lock and wait for the next buffer.
memcpy() – copy the shared buffer into a local buffer.
Validate – read each word out of the shared buffer and check its value in the incrementing sequence pattern.

## Slide 4: Simulated AMP Overview
In the simulated AMP example the application is run on the A9 dual core in SMP mode with core isolation such that the producer thread can be run with affinity on core 1 and the consumer thread is run with affinity on core 0. pthread_mutex_locks are not used here because we would not have that convenience in a true AMP environment, so these locks are replaced with a basic spinlock mechanism with locks allocated in DDR so that we can leverage the exclusivity monitor in the HMC. The producer thread writes incrementing values into the shared buffers to pass over to the consumer thread. Before passing the buffer the L1 cache is flushed and invalidated so that we have a coherent data exchange in the L2 cache. The consumer thread is then configured to operate in three different ways:
No Work – do nothing, simply release the buffer lock and wait for the next buffer.
memcpy() – copy the shared buffer into a local buffer.
Validate – read each word out of the shared buffer and check its value in the incrementing sequence pattern.
After the consumer thread is finished with the buffer the L1 cache is flushed and invalidated so that we have a coherent data exchange in the L2 cache.

## Slide 5: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
The SMP model for this example configures all of the locks and buffers such that they are inner cacheable. This allows the SMP cores to leverage the coherency hardware to expedite the lock exchanges and buffer exchanges.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 6: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
The relationship of the locks and buffers are as follows. Buffer 0 is owned by the thread that holds Lock 0 and Buffer 1 is owned by the thread that holds Lock 1. When a thread is finished with a buffer it must first acquire the sync lock before releasing the buffer lock. This ensures that each thread is holding at least one lock and prevents the other thread from sequencing past it. When a thread is holding the sync lock for one buffer it can then attempt to acquire the buffer lock for the next buffer. The slides that follow illustrate this sequencing.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 7: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
The threads are initialized very carefully using an additional lock not shown in this diagram. The consumer thread acquires Lock 1 sync and the producer thread acquires Lock 0. Each thread must always be holding one lock so that the other thread cannot pass it during the buffer exchanges.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 8: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Once the threads are initialized and holding their lock the processing sequence can begin. Since the producer thread holds Lock 0 it can now write into Buffer 0. The consumer thread continuously attempts to acquire Lock 0.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 9: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
When the producer thread has completed its work on Buffer 0 it then attempts to acquire Lock 0 sync.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 10: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
After the Producer thread acquires Lock 0 sync it may then release Lock 0.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 11: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Once Lock 0 is released by the Producer thread it can then be acquired by the Consumer thread.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 12: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
After the Consumer thread acquires Lock 0 it can release Lock 1 sync.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 13: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Once the Producer thread acquires Lock 0 sync it immediately attempts to acquire Lock 1.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 14: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
After the Producer thread acquires Lock 1 it can then release Lock 0 sync.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 15: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
At this point the consumer thread owns Buffer 0 and the Producer thread owns Buffer 1.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 16: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
The threads operate on their respective buffers.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 17: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Once each thread has completed its work on the buffer the Producer thread will attempt to acquire Lock 1 sync and the Consumer thread will attempt to acquire Lock 0 sync.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 18: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Once each thread acquires the sync lock it can then release the buffer lock.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 19: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Then each thread attempts to acquire the next buffer lock.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 20: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
After each thread acquires the next buffer lock it can release the sync lock that it was holding.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 21: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Now the Producer thread owns Buffer 0 and the Consumer thread owns Buffer 1 and they can each operate on their buffer.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 22: SMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
Once each thread has completed its buffer operations it then attempts to acquire the next sync lock. And the whole sequence repeats as the ping pong buffers are exchanged over and over.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 23: AMP model.
Inner
Cacheable
Non
Cacheable
Outer
Cacheable
Consumer
core0
The AMP model works exactly the same way that the SMP model works; however, the buffers must be allocated or managed as outer cacheable, and the locks must be allocated as non-cacheable. In this case the lock exchanges and buffer coherency is not assisted by the SMP hardware and must be managed by the software environment which consumes significant time.
Shared Memory Map
Producer
core1
Buffer 0
Lock 0 sync
Lock 1
Lock 0
Buffer 1
Lock 1 sync

## Slide 24: Interpreting the data.
The data that follows shows the performance that is achieved by the test application, measures of the number of megabytes per second that are transferred from one core to the other, as well as the number of lock exchanges per second that are accomplished. While the producer thread always performs the same task, filling the shared buffer with incrementing values, the consumer thread is operated in three different work profiles, one slide is presented for each work profile.
The X axis represents the number of words that the producer thread is asked to create. So the number of bytes exchanged is 4 times that value.

## Slide 25: No Work
Chart: MB/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 0 | 9.8328 | 19.4787 | 39.382 | 74.786 | 142.8318 | 261.2195 | 442.8903 | 698.9775 | 987.809 | 1262.694 | 1464.1279 | 1591.0128 | 1658.3086 | 1691.3203 | 1713.8219 | 1727.2224
AMP | 0 | 1.6409 | 3.2832 | 6.5194 | 12.6485 | 24.6528 | 46.5664 | 78.0904 | 91.5971 | 92.5054 | 100.994 | 106.8741 | 109.3007 | 110.4393 | 111.1038 | 111.4713 | 111.6139
Chart: MB/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 0 | 9.8328 | 19.4787 | 39.382 | 74.786 | 142.8318 | 261.2195 | 442.8903 | 698.9775 | 987.809 | 1262.694 | 1464.1279 | 1591.0128 | 1658.3086 | 1691.3203 | 1713.8219 | 1727.2224
AMP | 0 | 1.6409 | 3.2832 | 6.5194 | 12.6485 | 24.6528 | 46.5664 | 78.0904 | 91.5971 | 92.5054 | 100.994 | 106.8741 | 109.3007 | 110.4393 | 111.1038 | 111.4713 | 111.6139
Chart: Locks/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 5188500.4679 | 5155239.1845 | 5106220.6315 | 5161871.2851 | 4901177.9809 | 4680311.366 | 4279820.9111 | 3628157.1129 | 2863012.0135 | 2023032.8298 | 1292998.6351 | 749633.4774 | 407299.2829 | 212263.495 | 108244.502 | 54842.3021 | 27635.5589
AMP | 868996.3148 | 860316.0305 | 860665.2725 | 854508.9509 | 828933.5175 | 807823.7653 | 762943.6563 | 639716.7204 | 375181.5589 | 189451.003 | 103417.8281 | 54719.5455 | 27980.9778 | 14136.2356 | 7110.6425 | 3567.0826 | 1785.822
Chart: Locks/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 5188500.4679 | 5155239.1845 | 5106220.6315 | 5161871.2851 | 4901177.9809 | 4680311.366 | 4279820.9111 | 3628157.1129 | 2863012.0135 | 2023032.8298 | 1292998.6351 | 749633.4774 | 407299.2829 | 212263.495 | 108244.502 | 54842.3021 | 27635.5589
AMP | 868996.3148 | 860316.0305 | 860665.2725 | 854508.9509 | 828933.5175 | 807823.7653 | 762943.6563 | 639716.7204 | 375181.5589 | 189451.003 | 103417.8281 | 54719.5455 | 27980.9778 | 14136.2356 | 7110.6425 | 3567.0826 | 1785.822

## Slide 26: memcpy()
Chart: MB/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 0 | 8.1468 | 15.8631 | 31.0187 | 62.6972 | 120.9382 | 215.9168 | 377.128 | 611.4522 | 777.3767 | 915.3415 | 1003.4761 | 1053.2397 | 1103.2942 | 1365.1046 | 1418.5627 | 1368.3795
AMP | 0 | 1.6003 | 3.1699 | 6.3107 | 12.3786 | 23.413 | 45.4827 | 78.9095 | 129.6052 | 193.3491 | 254.95 | 302.9837 | 328.2806 | 272.7257 | 251.545 | 251.1295 | 310.4608
Chart: Locks/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 4378232.2927 | 4271244.2911 | 4158413.9418 | 4065676.676 | 4108922.7301 | 3962901.8336 | 3537581.2852 | 3089432.6378 | 2504508.0281 | 1592067.5164 | 937309.648 | 513779.7683 | 269629.3709 | 141221.6631 | 87366.6924 | 45394.0057 | 21894.0717
AMP | 856197.7663 | 839022.503 | 830964.4178 | 827160.5982 | 811242.3091 | 767196.2308 | 745188.6312 | 646426.6568 | 530862.8908 | 395978.8727 | 261068.7702 | 155127.6701 | 84039.8302 | 34908.8881 | 16098.8792 | 8036.1449 | 4967.3726
Chart: MB/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 0 | 8.1468 | 15.8631 | 31.0187 | 62.6972 | 120.9382 | 215.9168 | 377.128 | 611.4522 | 777.3767 | 915.3415 | 1003.4761 | 1053.2397 | 1103.2942 | 1365.1046 | 1418.5627 | 1368.3795
AMP | 0 | 1.6003 | 3.1699 | 6.3107 | 12.3786 | 23.413 | 45.4827 | 78.9095 | 129.6052 | 193.3491 | 254.95 | 302.9837 | 328.2806 | 272.7257 | 251.545 | 251.1295 | 310.4608
Chart: Locks/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 4378232.2927 | 4271244.2911 | 4158413.9418 | 4065676.676 | 4108922.7301 | 3962901.8336 | 3537581.2852 | 3089432.6378 | 2504508.0281 | 1592067.5164 | 937309.648 | 513779.7683 | 269629.3709 | 141221.6631 | 87366.6924 | 45394.0057 | 21894.0717
AMP | 856197.7663 | 839022.503 | 830964.4178 | 827160.5982 | 811242.3091 | 767196.2308 | 745188.6312 | 646426.6568 | 530862.8908 | 395978.8727 | 261068.7702 | 155127.6701 | 84039.8302 | 34908.8881 | 16098.8792 | 8036.1449 | 4967.3726

## Slide 27: Validate
Chart: MB/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 0 | 8.4625 | 16.5408 | 32.2046 | 58.7732 | 101.355 | 171.0202 | 254.8216 | 345.5257 | 420.2675 | 470.8268 | 501.1583 | 517.5782 | 501.876 | 451.4314 | 442.072 | 444.9711
AMP | 0 | 1.6107 | 3.1813 | 6.3337 | 11.8903 | 22.8393 | 41.5211 | 69.6067 | 99.329 | 73.4331 | 79.0505 | 81.7237 | 83.3959 | 84.7992 | 85.6016 | 86.0212 | 86.4234
Chart: Locks/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 4711630.7552 | 4436771.5334 | 4336068.6417 | 4221117.1367 | 3851757.9923 | 3321199.19 | 2801994.1941 | 2087498.889 | 1415273.0825 | 860707.9303 | 482126.5951 | 256593.0564 | 132500.023 | 64240.1308 | 28891.6103 | 14146.3047 | 7119.5376
AMP | 867322.5467 | 844493.3707 | 833964.6332 | 830174.6394 | 779243.9232 | 748398.2402 | 680281.8071 | 570218.2144 | 406851.6344 | 150391.0658 | 80947.6926 | 41842.5318 | 21349.3493 | 10854.2957 | 5478.5028 | 2752.68 | 1382.7747
Chart: MB/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 0 | 8.4625 | 16.5408 | 32.2046 | 58.7732 | 101.355 | 171.0202 | 254.8216 | 345.5257 | 420.2675 | 470.8268 | 501.1583 | 517.5782 | 501.876 | 451.4314 | 442.072 | 444.9711
AMP | 0 | 1.6107 | 3.1813 | 6.3337 | 11.8903 | 22.8393 | 41.5211 | 69.6067 | 99.329 | 73.4331 | 79.0505 | 81.7237 | 83.3959 | 84.7992 | 85.6016 | 86.0212 | 86.4234
Chart: Locks/s
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP | 4711630.7552 | 4436771.5334 | 4336068.6417 | 4221117.1367 | 3851757.9923 | 3321199.19 | 2801994.1941 | 2087498.889 | 1415273.0825 | 860707.9303 | 482126.5951 | 256593.0564 | 132500.023 | 64240.1308 | 28891.6103 | 14146.3047 | 7119.5376
AMP | 867322.5467 | 844493.3707 | 833964.6332 | 830174.6394 | 779243.9232 | 748398.2402 | 680281.8071 | 570218.2144 | 406851.6344 | 150391.0658 | 80947.6926 | 41842.5318 | 21349.3493 | 10854.2957 | 5478.5028 | 2752.68 | 1382.7747

## Slide 28: Performance Summary
These charts show the performance advantage that is achieved by the SMP implementation over the AMP simulation.
The average performance difference is:
NO WORK = 9.8x faster
MEMCPY = 4.6x faster
Validate = 5.1x faster
Chart: NO WORK
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP/AMP | 5.9707 | 5.9923 | 5.9329 | 6.0407 | 5.9126 | 5.7937 | 5.6096 | 5.6715 | 7.631 | 10.6784 | 12.5027 | 13.6996 | 14.5563 | 15.0156 | 15.2229 | 15.3746 | 15.475
Average | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282 | 9.8282
Chart: MEMCPY
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP/AMP | 5.1136 | 5.0907 | 5.0043 | 4.9152 | 5.065 | 5.1654 | 4.7472 | 4.7792 | 4.7178 | 4.0206 | 3.5903 | 3.312 | 3.2084 | 4.0454 | 5.4269 | 5.6487 | 4.4076
Average | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034 | 4.6034
Chart: Validate
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
SMP/AMP | 5.4324 | 5.2538 | 5.1993 | 5.0846 | 4.9429 | 4.4377 | 4.1189 | 3.6609 | 3.4786 | 5.7231 | 5.956 | 6.1324 | 6.2063 | 5.9184 | 5.2736 | 5.1391 | 5.1487
Average | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239 | 5.1239